## Slide 1: County Engineers Association of Maryland Fall Conference 2013
What Tragedy has Taught Us about Professionalism, Ethics, Leadership and Public Safety
Ed Link
Department of Civil and Environmental Engineering
University of Maryland

## Slide 2: Issue: Ethics in an Uncertain Future
Cannon 1: Engineers shall hold paramount the safety, health, and welfare of the public and shall strive to comply with the principles of sustainable development in the performance of their professional duties.
ASCE Code of Ethics

## Slide 3: Things That Lead to Ethical Engineering
Licensing
Design Standards
Best Practice
Review
Inspection
Monitoring
Values

## Slide 4: Things that Lead to Failure
Human Error
Compromise
  Resources
  Political Will
  Scale
What We Don’t Know
What We Don’t Know We Don’t Know

## Slide 5: The Challenger Disaster
Abnormally cold launch forecast
‘O’ Rings not verified for cold condition
Program behind schedule; re-bid approaching
Engineers said ‘no’, but…..
1986 Launch
7 astronauts killed
Notes: Thiokol's Bob Ebeling wrote the infamous 'Help!' memo in October 1985, informing everyone within his capabilities of the growing concerns about low temperature launches relating to the seals on the SRBs.
'We didn't think we were getting anyone's attention and we thought by using the subject 'Help!' would get them (Thiokol top level management) to read at least the first sentence of the memo,' said Ebeling.
'The entire Thiokol group recommended no launch,' remembered Ebeling, as they recommended a minimum launch temperature of 53F (11C). The expected rubber stamping of that recommendation was expected from NASA on the other end of the teleconference. However, they would be proven wrong.
'I thought it was a very poor briefing,' said Lovingood. 'To make such a huge statement on flight safety, it was an extremely poor briefing.' NASA engineers at MSFC started to pull apart Thiokol's data

## Slide 6: Traditional Deterministic Design
Physically Possible &
Reasonably Probable
Unreasonably Rare
Physically
Unreasonable
Improbable
Impossible
Design Point
Dr. D.N.D. Hartford, BC Hydro
High Forces + Low Resistance + Factor of Safety

## Slide 7: Emergence of Risk-Based Engineering
The expected value is the product of its probability and some measure of its severity.
Event probability
Event consequence
Portfolio of risks
Event
Rank-order
Risk = the expected value of an unwanted event which may or may not occur.

## Slide 8: What Have We Learned Lately?
Hurricane Katrina 2005
Missouri/Mississippi River Flooding 2011
Super Storm Sandy 2012

## Slide 10: New Orleans, Katrina, August 29, 2005

## Slide 11
The hurricane protection system was constructed piecemeal under multiple authorities and remained incomplete when Katrina struck
Notes: There were many part sto this system controlled ans built by many dififerent agencies
Seams were there and obviosu – post afacto
Levee- floodwall-gates, drainange not gamed as a while.
Whose sytem was it. Was it inspected as a system -no

## Slide 12: New Orleans Hurricane Protection System
Congress Authorizes Study
Congress Authorizes 70/30 cost sharing
Corps Recommends Barrier Plan
Hurricane Betsy
Federal Court halts project
Plan Reformulated
Corps Recommends high level plan
Congress Directs Parallel Protection Plan
Congress Authorizes Barrier Plan
Hurricane Katrina
Source: Hurricane Protection Decision Chronology Study

## Slide 13: The Protection System in part increased risk by encouraging development in vulnerable areas

## Slide 14
C
L
Deflection and
Pressure
Failure and
Movement
Confirmation in Centrifuge
Displacement of wall and part of levee
Design Criteria had not Considered Actual Failure Modes
Notes: Rsational on next page

## Slide 15
Publication (Year) Period of Record Meteorological Parameter |  | USWB Tech Report #33 (1959) 1900-56 | NWS Tech Report #23 (1979) 1900-1975 | NOAA/NCDC Prelim Analysis (2006) 1900-2005
100-year Central Pressure Index (millibars) |  | 934.6 mb | 926.2 mb | 901.7 mb
Return Period for Hurricane Katrina intensity storm (905 mb) |  | 900 years | 285 years | 98 years
The Hazard Was Underestimated

## Slide 16: What Does History Suggest?
1965 SPH = 12.4 ft,
1965 PMH = 15 ft,
Katrina = 20+ ft
Aug 28, 2005 - Katrina surge = 1000+ year event
Sep 1, 2005 - Katrina surge = 100 + year event

## Slide 17
Modern Hurricane Hazard
500-year peak surge
100-year peak surge

## Slide 18: New Barrier, IHNC/GIWW
Notes: New 1B plus navigable barrier at entrance to IHNC.

## Slide 19: 100-year vs 500-year Flood Depth Maps
500-year, W/Pumps
2007, 500-year, 50% Pump
500-year, W/Pumps
100-year, W/Pumps
2007, 100-year, 50% Pumps
100-year, W/Pumps
Pre-Katrina
2011 HSDRRS
IPET
Notes: 19

## Slide 20
The Mississippi Basin Drains 41% of the Contiguous United States
Mississippi River Basin
3.1 million km2
32% of total US farm acreage
Ohio
Missouri
Mississippi
Mississippi River
Length - 3730 km
Average flow – 12,700,000 m3/s
Max Flow -85,000 m3/s
Copyright ©2011 Omaha World-Herald®.

## Slide 21
Fort Peck
Garrison
Oahe
Big Bend
Fort Randall
Gavins Point
Main Stem
Reservoirs
Levees
and
Channels
Tributary
Reservoirs

## Slide 22
20,000 MM3

## Slide 23
(73,800 Mm3)

## Slide 24: b
1881 Flood of record
1844 Flood of Record

## Slide 25: Missouri River Basin - Annual Runoff above Sioux City, Iowa
1881 Flood = Design Criteria
1 Maf = 1233 Mm3
1%/97
.2%/97
.2%
1%

## Slide 28
The 12 Month Solution:
Federal Project - Levees, Floodways, Storage, River training, Dredging, Dikes, Dams
Navigation, Flood Control, Environment

## Slide 29
Three Storms Generate Project Design Storm
(No Snow Melt Considered)

## Slide 30: Project Design Flood
Morganza Floodway

## Slide 31
System: Reservoirs,
Levees, Floodways
and Backwater Areas
Notes: The Birds Point-New Madrid flood is one feature of the MR&T project.
The floodway was designed to prevent the project flood from exceeding the design elevation at and above Cairo and along east bank levee adjacent to the floodway.
The floodway boundaries are defined by the main stem MR&T project levee between Birds Point, Missouri, and New Madrid, Missouri, on the east and the setback levee on the west.
The 130,000-acre area within the floodway varies in width from about three to ten miles, has a length of nearly 35 miles. The floodway is designed to divert 550,000 cfs from the Mississippi River during the project flood and provides about seven feet of stage lowering in the vicinity of Cairo, with smaller reductions above Cairo and through the floodway reach.
The floodway has two fuseplug levees at its upper and lower end. The fuseplug sections are levees constructed to a lower height than the main stem levees. The floodway is placed into operation when the fuseplug levees are artificially crevassed. Under the current operating plan developed in 1986, the floodway is activated when sections of the frontline levee naturally overtop or are artificially crevassed. The floodway requires timely operation to insure its design effect during a flood approaching the project flood magnitude. In addition to natural overtopping, the plan of operation involves the placing and detonation of explosives at critical locations.

## Slide 32
Observed Apr 19-May 4 2011
Precipitation
Total PDF Precipitation
  PDF occurred in 3 weather events.
    The 2011 event occurred during 2 rainfall events 4/19-4/28 and 5/1-5/4 plus snowmelt
    Stages at Cairo were elevated (+10ft or 127% of normal) at the onset of the 2011 rainfall event
69 % of PDF Rainfall
Plus major snow melt

## Slide 33
(68,000 km2)
(26,300 km2)
(40,500 km2)
80 % PDF Flow
55 % Floodway
Capacity Used
20 % Backwater
Storage Used
Historic High
Discharges
above NOLA

## Slide 34
Hurricane Sandy
X

## Slide 37
Category 5 over ocean, weakened to Category 3 by landfall
200-year hurricane
500 miles wide
Storm surge 14-18 ft
600 Fatalities
$18 B Damages
The Long Island Express
September 19-21, 1938

## Slide 40
SANDY, Oct 2012

## Slide 42
January 24, 2013

## Slide 44: Ocean Gate, N.J., November 2012
Photo - FEMA

## Slide 46: What Have We Learned Lately
Hurricane Katrina 2005
  Lack of External Peer Review
  Risk and Uncertainty (Societal versus Nature)
  Outdated Hazard (forces)
  Outdated Standards, Failure Modes
  Need Complete Systems (and Resources)
Missouri/Mississippi River Flooding 2011
  Conservative Criteria can counter Surprise
  Multi-Purpose can Dilute Extreme Event Performance
  Value of Redundancy and Robustness
  Need Complete System
  Challenge of using history as a basis for Design (1881/1844)
Super Storm Sandy 2012
  High Cost of Lack of Anticipation and Preparedness
  Rare Event
  Difficulty in undoing decades of land use practice
  Complexities of collaborative solutions
  The need to plan and adapt long term
Perhaps the Greatest Challenges Lie Ahead

## Slide 47: A new study points to the rapidly escalating risk of Sandy-magnitude flooding events in the New York City area. The study, published Thursday in the Bulletin of the American Meteorological Society, found that sea level rise has already doubled the annual probability of a Sandy-level flood in New York City since 1950.
a new study by researchers from Columbia University and Colorado State University is suggesting climate change could eventually keep such hurricanes from making a sizeable impact on US coastlines. Publishing the findings in the journal Proceedings of the National Academy of Sciences ….
Hurricanes Become Less Threatening To US Coast, Based On Climate Models
Climate Change Doubles Likelihood of Sandy-Level Floods in NYC
Going Forward

## Slide 48
Krusik & Cook (2004) North American Drought Atlas
800
900
1000
1100
1700
1800
1900
2000
1200
1300
1400
1500
1600
Western US Drought Area Index (-1 PDSI)
80 yr lowpass
Medieval Warm Period
Little Ice Age
Percent Area of Drought (<-1 PDSI)
Current drought occurrence in the western U.S. is approaching that of the Medieval Warm Period.

## Slide 50: A SEA LEVEL RISE RESPONSE STRATEGY FOR THE STATE OF MARYLAND
Zoë Pfahl Johnson
NOAA Coastal Management Fellow
for
Maryland Department of Natural Resources
Coastal Zone Management Division
October, 2000
Website: www.dnr.state.md.us

## Slide 52: Updating Maryland’s Sea-level Rise Projections
Scientific and Technical Working Group
Maryland Climate Change Commission
June 26, 2013
Current Inundation
6 ft SLR Inundation

## Slide 53
Sea Level Rise Response Strategy
Worcester County, Maryland
September 2008
Worcester County, Maryland
Department of Comprehensive Planning
1 West Market Street
Snow Hill, Maryland 21863-1249

## Slide 54: What Does This Mean Going Forward?
Embracing risk and uncertainty
Continually changing standards and practice
Continuous education
Integrated systems solutions across physical and political boundaries
Adaptive life-cycle management
Just-in-time or continuous peer review

## Slide 55: Philosophy
In times of change, learners inherit the Earth, while the learned find themselves beautifully equipped to deal with a world that no longer exists.
Eric Hoffer